## Slide 1: Friction Drag
Friction drag, also known as skin friction drag
is caused by the friction of a fluid against the surface of an object that is moving through it.
It is directly proportional to the area of the surface in contact with the fluid and increases with the square of the velocity.

## Slide 2
Friction Drag is created in the boundary layer due to the viscosity of the air and the resulting friction against the surface of the aircraft.
In practice the extent of retardation and skin friction drag depends on the rate at which air adjacent to the surface is trying to slide relative to it. This produces a shear stress between adjacent air particles, which is directly proportional to the speed of the airflow.

## Slide 3
Friction Drag is created in the boundary layer due to the viscosity of the air and the resulting friction against surface of the aircraft.

## Slide 4
The air molecules in direct contact with the aircraft surface are most affected.
As the molecules flow past the surface and past each other, the viscous resistance to that flow becomes a force which retards forward motion.
The amount of friction drag that is created per square meter of surface area is relatively small.

## Slide 5
Turbulent flow creates more friction drag than laminar flow due to its greater interaction with the surface of the airplane.
Rough surfaces accelerate the boundary layer airflow from laminar to turbulent. This increases boundary layer thickness and the airflow disruption within the boundary layer

## Slide 6
These increases result in more air molecules being affected by the movement of the aircraft and a corresponding increase in friction drag.
Friction drag can be reduced by delaying the point at which laminar flow becomes turbulent.

## Slide 7
This can be accomplished by smoothing the exposed surfaces of the aircraft by using flush rivets on the leading edges and through painting, cleaning, waxing, polishing or the application of surface coatings.