## Slide 1: Interference Drag
Interference drag is generated by the mixing of airflow streamlines between airframe components such as the wing and the fuselage, the engine pylon and the wing or, in the case of a military or other special purpose aircraft, between the airframe and attached external stores such as fuel tanks, weapons or sensor pods.

## Slide 2
Interference drag is generated when the airflow across one component of an aircraft is forced to mix with the airflow across an adjacent or proximal component.
If one considers two parts of the aircraft that intersect at a particular point, such as the vertical and horizontal components of the empennage, it is obvious where the point of intersection occurs.

## Slide 3
At the intersection of the two surfaces, there is less physical space for the airflow to occupy resulting in the turbulent mixing of the two airflows and the production of a localized shock wave.
Due to this shock wave, the resulting total drag from the empennage is greater than the sum of the drag produced individually by the vertical tail and the horizontal tail surfaces.

## Slide 4
Other significant locations which generate interference drag include the wing/fuselage junction and the wing/engine pylon or fuselage/engine pylon convergence.

## Slide 5
interference drag can be minimized by the appropriate use of fairings and fillets to ease the transition between components.
Fairings and fillets use curved surfaces to soften the transition at the junction of two aircraft components
This, in turn, allows the airflow streamlines to meet gradually rather than abruptly and reduces the amount of interference drag that is generated.

## Slide 6: INDUCED DRAG
Induced Drag is an inevitable consequence of lift and is produced by the passage of an airfoil (e.g. wing or tailplane) through the air.
Air flowing over the top of a wing tends to flow inwards because the decreased pressure over the top surface is less than the pressure outside the wing tip.

## Slide 7
Below the wing, the air flows outwards because the pressure below the wing is greater than that outside the wing tip.
A direct consequence of this is that there is a continual spilling of air upwards around the wing tip phenomenon called ‘tip effect’ or ‘end effect’.

## Slide 8
One way to appreciate why a high aspect ratio for a wing is better than a low one is that with a high aspect ratio, the proportion of air which moves in this way is reduced and therefore more of it generates lift.

## Slide 9
For the wing more generally, since the streams of air from above and below the wing which meet along the trailing edge are flowing at an angle to each other as they meet, they combine to form vortices, which, when viewed from the rear, rotate clockwise from the left wing and counter clockwise from the right.

## Slide 10
Although there must always be at least some induced drag because wings have a finite thickness, designers attempt wherever possible to reduce this flow. A required wing area can be achieved using different wing span-to-chord ratios (aspect ratios). The larger the wing aspect ratio, the less air disturbance is created at the tip.

## Slide 11
for most aircraft, there are both practical limits to maximum wing span for ground maneuvering and structural issues which mean that eventually, the weight penalty to adequately strengthen a long thin wing becomes excessive. The fact that aircraft carry most of their fuel in the wings is also a factor in wing design. Typical transport aircraft aspect ratios range between 6:1 and 10:1.

## Slide 12
Other ways to reduce induced drag and tip vortex strength in a wing design are also based upon reducing the quantity air movement upwards at the wing tip by aiming to generate relatively more of the lift away from tips

## Slide 13
Wing taper towards the tip assists this as does wing twist. The Boeing 767 is a example of a twisted wing. The inner wing is set at a higher angle of attack than the outer wing and thus generates proportionately more lift whereas the tip, at a very small angle of attack generates very little.

## Slide 14
Winglets have also become popular, including both the usual up-turned versions and the Airbus 320 series twoway ‘wingtip fence’ versions.
Well designed winglets can prevent about 20% of the airflow spillage at the tip, and therefore 20% of the induced drag